## Slide 1: Feasibility Study of BS Magnets Vacuum Chambers
W. Weterings

## Slide 2: Inside vacuum proposal from previous meeting
No Space for PSB
Down-Stream bellow
Recess flanges
Chamfer for access

## Slide 3
In-situ welding
compact “welded Bellows”
no space for QD flanges
Bolted Flange on tank
Flange bolted on tank not desirable

## Slide 4: New proposal with DN135 QD Flanges
No Space for PSB
Down-Stream bellow
Recess flanges
Chamfer for access

## Slide 5
No In-situ welding
DN135 QD flanges
But still issue of Bake-out & maintenance

## Slide 6: Initial design of BS Magnets with undulated Inconel chambers

## Slide 7: Conclusion PSB beam dynamics WG meeting on 19th November:
Eddy current effects in corrugated INCONEL chamber during (5ms) chicane fall an issue
  Make sure that delays between different BS magnets are not too different
  Sextupolar components not an issue!!
  Perturbation due to quadrupolar components by feed‐down
    Sizable (a bit smaller than edge focusing by BS magnets)
    Should be taken into account for compensation (in particular for injections with the vertical tune above the half‐integer resonance)
ProbabIy not (yet?) the end for BS magnets around
corrugated chambers … can one improve the situation?
What about ceramic vacuum chambers (see discussion with
J. Borburgh)?

## Slide 8: BS magnets with ceramic chambers - 1
BS1
BS2-3
BS4

## Slide 9
BS magnets with ceramic chambers - 2

## Slide 10
BS magnets with ceramic chambers - 3

## Slide 11
BS magnets with ceramic chambers - 4
Possible
Solution

## Slide 12: Conclusion
Inside Vacuum Tanks
  Feasible, but….
    Large bulky tanks
    Bake-out required
    Intervention difficult and time-consuming
Undulated Inconel Chambers
  Feasible, but….
    Eddy current effects
    Optics perturbations
Ceramic Chambers
  Feasible, but….
    Aperture restrictions for BS1
    Procurement / Price of ceramic chambers
    Fragile