## Slide 1: H0/H- beam Dump for LINAC4 PS BOOSTER INJECTION
Jan Borburgh
Brennan Goddard
Wim Weterings

## Slide 2: Position and dimensions
For space reasons extraction of H0/H- is excluded.
H0/H- dump will be inside the vacuum chamber of BS4 magnet.
The dump must provide:
  unobstructed passage for circulating beam during injection as well as the injected proton beam.
  optimum protection of the downstream elements.
BS1 BS2 BS3 BS4
Internal Dump

## Slide 3: AVAILABLE SPACE
The dump is close to the horizontal aperture limit in the injection region.
The total uncertainty of installed position of the dump edge < ±1 mm,
(including all mechanical, alignment and thermal tolerances.)

## Slide 4: Loading Assumption - 1
Nominal Operation
A continuous load at 1.11Hz with stripping efficiency of 98% :
Annual load on the dump, for 200 days (1.73∙107 sec) of operation:
For a period of ~8 hours a continuous power load at 1.11Hz with stripping efficiency of 90% :
This may happen about 10 times a year, resulting in a load of:

## Slide 5: Loading Assumption - 2
Accidental Failure
Foil failure or injection with no foil present -> impact of a 100μs slice on the H0/H- beam dump: 2.5∙1013p+@ 160 MeV (~500J).
Distributor failure combined with foil failure will not be considered in the design and shall be prevented by interlocking and careful design of the distributer triggering.

## Slide 6: material restrictions
The material must be completely non-magnetic….
…Or by its design induced very small eddy currents. (highly resistive material, segmentation, location outside the magnetic field).
Perturbation of the BS4 magnetic field < 1%.
  Time-varying field simulation are required to ensure that these conditions are respected.
    Decision of fast (0.5 ms) fall time version of the BS chicane or fall times of around 5 ms both still to be taken.
The material should be at least slightly conducting to avoid electrical charging on the material surface and in the bulk.
  Carbon, bulk resistivity ~ 1-510-5 Wm would be acceptable
  h-BN , bulk resistivity ~ 106– 1011 Wm, would be too good an insulator.

## Slide 7: mechanical & thermal constraints
The dump element must be supported in the yoke without recourse to internal fixings, supporting the dump by a system on the exit face of the magnet is conceivable.
The dump must withstand the pulsed magnetic field of 0.34 T and any residual vibration induced by the magnet pulsing.
It must also withstand repeated bake-out cycles of the magnet.
The design shall take into account the evacuation of 14.2 W (71W peak) heat generation in the dump.

## Slide 8: Integrated instrumentation
The H0/H- beam dump current is an important parameter, and should be monitored if feasible within the constraints listed above.
  To monitor the impacting beam current, the H0/H- beam dump should be electrically isolated from the BS4 magnet and from earth.
  To be able to measure the neutral H0 beam, a thin stripping element should be placed just before the dump.
A schematic possible current monitor:

## Slide 9
DRAFT